## Slide 1: Real Time Operating System “FreeRTOS” Interrupt Management
Using the FreeRTOS Real Time Kernel - a Practical Guide - Cortex M3 Edition (FreeRTOS Tutorial Books)
by Richard Barry
Sherif Hammad

## Slide 2: Agenda
How Embedded real-time systems have to take actions in response to events that originate from the environment (Interrupt Event Based)
Which FreeRTOS API functions can be used from within an ISR.
How a deferred interrupt scheme can be implemented.
How to create and use binary semaphores and counting semaphores.

## Slide 3: Deferred Interrupt Processing Binary Semaphores Used for Synchronization
A Binary Semaphore can be used to unblock a task each time a particular interrupt occurs
Binary Semaphore synchronizes the task with the interrupt.
This allows the majority of the interrupt event processing to be implemented within the synchronized task
Only a very fast and short portion remaining directly in the ISR.
The interrupt processing is said to have been ‘deferred’ to a ‘handler’ task.

## Slide 4: Deferred Interrupt Processing Binary Semaphores Used for Synchronization
If the interrupt processing is particularly time critical, then the handler task priority can be set to ensure that the handler task always pre-empts the other tasks in the system.
The ISR can then be implemented to include a context switch to ensure that the ISR returns directly to the handler task when the ISR itself has completed executing.
This has the effect of ensuring that the entire event processing executes contiguously in time, just as if it had all been implemented within the ISR itself.

## Slide 5: Deferred Interrupt Processing Binary Semaphores Used for Synchronization

## Slide 6: Deferred Interrupt Processing Binary Semaphores Used for Synchronization
The handler task uses a blocking ‘take’ call to a semaphore as a means of entering the Blocked state to wait for the event to occur.
When the event occurs, the ISR uses a ‘give’ operation on the same semaphore to unblock the task so that the required event processing can proceed.
In this interrupt synchronization scenario, the binary semaphore can be considered conceptually as a queue with a length of one. The queue can contain a maximum of one item at any time, so is always either empty or full (hence, binary). By calling xSemaphoreTake()
The handler task effectively attempts to read from the queue with a block time, causing the task to enter the Blocked state if the queue is empty.
When the event occurs, the ISR uses the xSemaphoreGiveFromISR() function to place a token (the semaphore) into the queue, making the queue full. This causes the handler task to exit the Blocked state and remove the token, leaving the queue empty once more.
When the handler task has completed its processing, it once more attempts to read from the queue and, finding the queue empty, re-enters the Blocked state to wait for the next event.

## Slide 7: Deferred Interrupt Processing Binary Semaphores Used for Synchronization

## Slide 8: Example 12. Using a binary semaphore to synchronize a task with an interrupt
This example uses a binary semaphore to unblock a task from within an interrupt service routine—effectively synchronizing the task with the interrupt.
A simple periodic task is used to generate an interrupt every 500 milliseconds.
A software generated interrupt is used because it allows the time at which the interrupt occurs to be controlled, which in turn allows the sequence of execution to be observed more easily.
The interrupt service routine, which is simply a standard C function.
It does very little other than clear the interrupt and ‘give’ the semaphore to unblock the handler task.

## Slide 9: Example 12. Using a binary semaphore to synchronize a task with an interrupt
The macro portEND_SWITCHING_ISR() is part of the FreeRTOS Cortex-M3 port and is the ISR safe equivalent of taskYIELD().
It will force a context switch only if its parameter is not zero (not equal to pdFALSE).
Note how xHigherPriorityTaskWoken is used. It is initialized to pdFALSE before being passed by reference into xSemaphoreGiveFromISR()
it will get set to pdTRUE only if xSemaphoreGiveFromISR() causes a task of equal or higher priority than the currently executing task to leave the blocked state. portEND_SWITCHING_ISR() then performs a context switch only if xHigherPriorityTaskWoken equals pdTRUE.

## Slide 10: Example 12. Using a binary semaphore to synchronize a task with an interrupt

## Slide 11: Example 12. Using a binary semaphore to synchronize a task with an interrupt

## Slide 12: Example 12. Using a binary semaphore to synchronize a task with an interrupt

## Slide 13: Example 12. Using a binary semaphore to synchronize a task with an interrupt

## Slide 14: Example 12. Using a binary semaphore to synchronize a task with an interrupt