## Slide 1: Real Time Operating System “FreeRTOS” Resource Management
Using the FreeRTOS Real Time Kernel - a Practical Guide - Cortex M3 Edition (FreeRTOS Tutorial Books)
by Richard Barry
Sherif Hammad

## Slide 2: Agenda
When and why resource management and control is necessary.
What a critical section is.
What mutual exclusion means.
What it means to suspend the scheduler.
How to use a mutex.
What priority inversion is, and how priority inheritance can reduce (but not remove) its impact.
What is DeadLock?

## Slide 3: Why Resource Management
In a multitasking system, there is potential for conflict if one task starts to access a resource, but does not complete its access before being transitioned out of the Running state.
“Resource Data” could be corrupted in the following cases:
  Accessing Peripherals: Consider the following scenario where two tasks attempt to write to an LCD:
    Task A executes and starts to write the string “Hello world” to the LCD.
    Task A is pre-empted by Task B after outputting just the beginning of the string—“Hello w”.
    Task B writes “Abort, Retry, Fail?” to the LCD before entering the Blocked state.
    Task A continues from the point at which it was pre-empted and completes outputting the remaining characters—“orld”.
    The LCD now displays the corrupted string “Hello wAbort, Retry, Fail?orld”.

## Slide 4: Why Resource Management
Read, Modify, Write Operations: This is a ‘non-atomic’ operation because it takes more than one instruction to complete and can be interrupted. Consider the following scenario where two tasks attempt to update a variable called GlobalVar:
  Task A loads the value of GlobalVar into a register—the read portion of the operation.
  Task A is pre-empted by Task B before it completes the modify and write portions of the same operation (before ORR instruction)
  Task B updates the value of GlobalVar, then enters the Blocked state.
  Task A continues from the point at which it was pre-empted. It modifies/corrupts the copy of the GlobalVar value calculated by Task B
Non-atomic Access to Variables:
  Updating multiple members of a structure
  Updating a variable that is larger than the natural word size of the architecture (for example, updating a 64-bit variable on a 32-bit machine)

## Slide 5: Why Resource Management
Function Reentrancy
  A function is reentrant if it is safe to call the function from more than one task, or from both tasks and interrupts.
  Each task maintains its own stack and its own set of core register values. If a function does not access any data other than data stored on the stack or held in a register, then the function is reentrant.

## Slide 6: Basic Critical Sections

## Slide 7: Basic Critical Sections
Critical sections implemented in this way are a very crude method of providing mutual exclusion.
They work by disabling interrupts up to the interrupt priority set by configMAX_SYSCALL_INTERRUPT_PRIORITY.
Pre-emptive context switches can occur only from within an interrupt.
As long as interrupts remain disabled, the task that called taskENTER_CRITICAL() is guaranteed to remain in the Running state until the critical section is exited.
Critical sections must be kept very short; otherwise, they will adversely affect interrupt response times.
Every call to taskENTER_CRITICAL() must be closely paired with a call to taskEXIT_CRITICAL().

## Slide 8: Suspending (or Locking) the Scheduler
Critical sections can also be created by suspending the scheduler.
Basic critical sections protect a region of code from access by other tasks and by interrupts.
A critical section implemented by suspending the scheduler protects a region of code only from access by other tasks because interrupts remain enabled.
FreeRTOS API functions should not be called while the scheduler is suspended.

## Slide 9: Suspending (or Locking) the Scheduler

## Slide 10: Mutexes (and Binary Semaphores)
In a mutual exclusion scenario: the mutex can be thought of as a token associated with the shared resource.
For a task to access the resource legitimately, it must first successfully ‘take’ the token (be the token holder).
When the token holder has finished with the resource, it must ‘give’ the token back.
Only when the token has been returned can another task successfully take the token and then safely access the same shared resource.
A task is not permitted to access the shared resource unless it holds the token.
A semaphore that is used for mutual exclusion must always be returned.
A semaphore that is used for synchronization is normally discarded and not returned.
There is no reason why a task cannot access the resource at any time, but each task ‘agrees’ not to do so, unless it is able to become the mutex holder.

## Slide 11: Mutexes (and Binary Semaphores)

## Slide 12: Mutexes (and Binary Semaphores)

## Slide 13: Mutexes (and Binary Semaphores)

## Slide 14: Mutexes (and Binary Semaphores)

## Slide 15: Mutexes (and Binary Semaphores)

## Slide 16: Mutexes (and Binary Semaphores) Priority Inversion
The higher priority Task 2 having to wait for the lower priority Task 1 to give up control of the mutex.
A higher priority task being delayed by a lower priority task in this manner is called ‘priority inversion’.
This undesirable behavior would be exaggerated further if a medium priority task started to execute while the high priority task was waiting for the semaphore—the result would be a high priority task waiting for a low priority task without the low priority task even being able to execute.
Priority inversion can be a significant problem, but in small embedded systems it can often be avoided at system design time, by considering how resources are accessed.

## Slide 17: Mutexes (and Binary Semaphores) Priority Inversion

## Slide 18: Mutexes (and Binary Semaphores) Priority Inheritance
FreeRTOS mutexes and binary semaphores are very similar “BUT”
Mutexes include a basic ‘priority inheritance’ mechanism
Binary semaphores do not.
Priority inheritance is a scheme that minimizes the negative effects of priority inversion but does not ‘fix’ priority inversion
Priority inheritance works by temporarily raising the priority of the mutex holder to that of the highest priority task that is attempting to obtain the same mutex.
The low priority task that holds the mutex ‘inherits’ the priority of the task waiting for the mutex.
The priority of the mutex holder is reset automatically to its original value when it gives the mutex back.

## Slide 19: Mutexes (and Binary Semaphores) Priority Inheritance

## Slide 20: Mutexes (and Binary Semaphores) Deadlock (or Deadly Embrace)
‘Deadlock’ (‘deadly embrace’) is another potential pitfall that can occur when using mutexes for mutual exclusion.
Deadlock occurs when two tasks cannot proceed because they are both waiting for a resource that is held by the other.
Consider the following scenario where Task A and Task B both need to acquire mutex X and mutex Y in order to perform an action:
  1. Task A executes and successfully takes mutex X.
  2. Task A is pre-empted by Task B.
  3. Task B successfully takes mutex Y before attempting to also take mutex X—but mutex X is held by Task A, so is not available to Task B. Task B opts to enter the Blocked state to wait for mutex X to be released.
  4. Task A continues executing. It attempts to take mutex Y—but mutex Y is held by Task B, so is not available to Task A. Task A opts to enter the Blocked state to wait for mutex Y to be released. At the end of this scenario, Task A is waiting for a mutex held by Task B, and Task B is waiting for a mutex held by Task A.