## Slide 1: Real Time Operating System “FreeRTOS” Interrupt Management Counting Semaphores/Queues
Using the FreeRTOS Real Time Kernel - a Practical Guide - Cortex M3 Edition (FreeRTOS Tutorial Books)
by Richard Barry
Sherif Hammad

## Slide 2: Agenda
Binary semaphore pitfall
Counting semaphore handling of fast interrupts (Example 13)
Sending/Receiving to Queues from ISR (Example 14)

## Slide 3: Binary Semaphore Pitfall
Binary Semaphore Synchronization
(Maximum One Pending Interrupt)

## Slide 4: Counting Semaphore
Counting Semaphore Synchronization

## Slide 5: Counting Semaphore
Counting events
  An event handler will 'give' a semaphore each time an event occurs—causing the semaphore’s count value to be incremented on each ‘give’.
  A handler task will 'take' a semaphore each time it processes an event—causing the semaphore’s count value to be decremented on each take.
  The count value is the difference between the number of events that have occurred and the number that have been processed.
  Counting semaphores that are used to count events are created with an initial count value of zero.
Resource management.
  The count value indicates the number of resources available.
  To obtain control of a resource a task must first obtain a semaphore—decrementing the semaphore’s count value.
  When the count value reaches zero, there are no free resources.
  When a task finishes with the resource, it 'gives' the semaphore back—incrementing the semaphore’s count value.
  Counting semaphores that are used to manage resources are created so that their initial count value equals the number of resources that are available.
Counting Semaphore; Use Cases

## Slide 6: Counting Semaphore
uxMaxCount: The maximum value the semaphore will count to.
  uxMaxCount value is effectively the length of the “queue”.
  When the semaphore is to be used to count or latch events, uxMaxCount is the maximum number of events that can be latched.
  When the semaphore is to be used to manage access to a collection of resources, uxMaxCount should be set to the total number of resources that are available.
uxInitialCount: The initial count value of the semaphore after it has been created.
  When the semaphore is to be used to count or latch events, uxInitialCount should be set to zero—as, presumably, when the semaphore is created, no events have yet occurred.
  When the semaphore is to be used to manage access to a collection of resources, uxInitialCount should be set to equal uxMaxCount—as, presumably, when the semaphore is created, all the resources are available.
Counting Semaphore; FreeRtos API

## Slide 7: Counting Semaphore; Example 13
Counting Semaphore; Example 13

## Slide 8: Using Queues within an Interrupt Service Routine
pxHigherPriorityTaskWoken It is possible that a single queue will have one or more tasks blocked on it waiting for data to become available.
Calling xQueueSendToFrontFromISR() or xQueueSendToBackFromISR() can make data available, and so cause such a task to leave the Blocked state.
If calling the API function causes a task to leave the Blocked state, and the unblocked task has a priority equal to or higher than the currently executing task (the task that was interrupted), then, internally, the API function will set *pxHigherPriorityTaskWoken to pdTRUE.

## Slide 9: Using Queues within an Interrupt Service Routine; Example 14

## Slide 10: Using Queues within an Interrupt Service Routine; Example 14

## Slide 11: Using Queues within an Interrupt Service Routine; Example 14

## Slide 12: Using Queues within an Interrupt Service Routine; Example 14

## Slide 13: Using Queues within an Interrupt Service Routine; Example 14